## Slide 1: 4 bit multiplier Circuit
Lisa Jacklin

## Slide 2: Planned Attack
VHDL
C++/C
Assembly

## Slide 3: VHDL Code and Circuits

## Slide 4: VHDL Subcircuits
Top Row Boxes
U(x) signals
Second and Third Row Boxes
W(x)/N(x) signals

## Slide 5
Top Row Code
ENTITY Fig1B IS
PORT ( M1, M2, Q0, Q1, Cin :In STD_LOGIC;
Cout, S :OUT STD_LOGIC);
END ENTITY;
ARCHITECTURE Block1 OF Fig1B IS
COMPONENT Adder IS
PORT (X1, X2, Cin : IN STD_Logic ; --x and y are inputs of the adder
Cout, S :BUFFER STD_Logic); --c is the carry and s is the sum value
END COMPONENT;
SIGNAL A1, A2, A3 :STD_LOGIC;
BEGIN
A1 <= M1 AND Q0;
A2 <= M2 AND Q1;
A4:Adder PORT MAP (X1 => A1, X2 => A2, Cin => Cin, --INPUTS
Cout => Cout, S => s); --OUTPUT VALUES FROM ADDER
END ARCHITECTURE;
Second and Third Row Code
ENTITY Fig1C IS
PORT ( M1, cc, Q1, Cin :In STD_LOGIC;
Cout, S :OUT STD_LOGIC);
END ENTITY;
ARCHITECTURE Block2 OF Fig1C IS
COMPONENT Adder IS
PORT (X1, X2, Cin : IN STD_Logic ; --x and y are inputs of the adder
Cout, S :BUFFER STD_Logic); --c is the carry and s is the sum value
END COMPONENT;
SIGNAL A1 :STD_LOGIC;
BEGIN
A1 <= M1 AND Q1;
A2:Adder PORT MAP (X1 => A1, X2 => cc, Cin => Cin, --inputs
Cout => Cout, S => s); --outputs
END ARCHITECTURE;

## Slide 6: VHDL Full Adder Subcircuit
Entity Adder IS
Port (X1, X2, Cin : IN STD_Logic ; --x and y are inputs of the adder
Cout,S :BUFFER STD_Logic); --c is the carry and s is the sum value
End Adder;
Architecture Adder_Circuit Of Adder is
Signal a1, a2, a3, a4, a5: std_logic;
Begin
a1<=X1 XOR X2;
a2<=x1 XoR Cin;
a3<=x1 AND Cin;
a4<= x2 AND Cin;
a5<= x1 AND x2;
Cout <= a5 or a3 or a4;
S <= a1 xor cin;
End Adder_Circuit;
Adder Code
void Adder(char x, char y, char cin) {
//output integers...
char Co;
char s;
  //these give the carry out and sum value for the adder...
  //condensed version of the signals
  Co = (x & y) | (y & cin) | (x & cin);
  s = cin ^ (x ^ y);
  //test display to verify adder
  //std::cout << Co << s << "\n"; //be careful and make sure to check
};

## Slide 7: ASM Full Adder Subcircuit
Adder:
;the values for r8 and r9 are given by the the other subcircuits values
cmp r8, 0
jg Sum
cmp r9, 0
jg Sum
Sum:
cmp r8, r9
je Equal
jg SumNoCout
jl SumNoCout
SumNoCout:
mov r10, 1 ; sum value is one
mov r11, 0
Equal:
mov r11, 1 ; this is the carry value,
mov r10, 0 ; and this is the corresponding sum value

## Slide 8: Multiplier Top Circuits in CPP/asm
void Fig1B(char x, char x2, char cin, char y, char y2) {
//signals
char a1 = x & y;
char a2 = x2 & y2;
Adder(a1, a2, cin);
};
TopRow:;fig1b top row values
;first two values
;ADD IN CARRY LATER
mov rax, M ;set to M array mov rdi, Q ; set to Q array
mov r8, QWORD[rcx]
mov r9, QWORD[rcx+16]
;second two values
mov r10, QWORD[rdi+24]
mov r11, QWORD[rdi+16]
cmp r8, r11
je Adder
cmp r9, r10
je Adder
Cpp
ASM

## Slide 9: Multiplier Other Rows Circuits in CPP/ASM
void Fig1C(char x, char cc, char y, char cin) {
//signal again
char a1 = x & y;
Adder(a1, cc, cin);
};
SecondRow:
mov rax, M
mov rdi, Q
mov rcx, Cout
;this is where the carry values ;come in...so Cout, PP1, and PP2
mov r8, QWORD[rax]
mov r9, QWORD[rdi]
cmp r8,r9
je A1 ;
cmp r8, rcx ;x1 = M and x2 = cout jmp Adder
Cpp
ASM

## Slide 10: Where things went wrong

## Slide 11: VHDL PortMap
u1: Fig1B PORT MAP ( M(0), M(1), Q(1), Q(0), '0', Cout(0), P(1));
u2: Fig1B PORT MAP ( M(1), M(2), Q(1), Q(0), Cout(0), Cout(1), PP1(2));
u3: Fig1B PORT MAP ( M(2), M(3), Q(1), Q(0), Cout(1), Cout(2), PP1(3));
u4: Fig1B PORT MAP ( M(3), '0', Q(1), Q(0), Cout(2), PP1(5), PP1(4));
--Second row
w1:Fig1C PORT MAP (M(0),PP1(2),Q(2),'0',Cout(3),P(2));
w2:Fig1C PORT MAP (M(1),PP1(3),Q(2),Cout(3),Cout(4),PP2(3));
w3:Fig1C PORT MAP (M(2),PP1(4),Q(2),Cout(4),Cout(5),PP2(4));
w4:Fig1C PORT MAP (M(3),PP1(5),Q(2),Cout(5),PP2(6),PP2(5));
--Last line, final output values, P
N1:Fig1C PORT MAP (M(0),PP2(3),Q(3),'0',Cout(6),P(3));
N2:Fig1C PORT MAP (M(1),PP2(4),Q(3),Cout(6),Cout(7),P(4));
N3:Fig1C PORT MAP (M(2),PP2(5),Q(3),Cout(7),Cout(8),P(5));
N4:Fig1C PORT MAP (M(3),PP2(6),Q(3),Cout(8),P(7),P(6));

## Slide 12: Future Considerations
Try a different approach
01
Make my own templates that allow for various values input and output and preliminary
02
Maybe try writing my own multiply in assembly
03

## Slide 13: Thank You